## Slide 1: Processor
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
See P&H Chapter: 2.16-2.20, 4.1-4.4, Appendix B
Notes: Old See P&H Chapter 2.16-20, 4.1-4

## Slide 2: Announcements
Project Partner finding assignment on CMS
Office hours over break

## Slide 3: Announcements
Make sure to go to your Lab Section this week
Lab2 due in class this week (it is not homework)
Lab1: Completed Lab1 due this Friday, Feb 13th, before winter break
Note, a Design Document is due when you submit Lab1 final circuit
Work alone
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
Homework1 is out
Due a week before prelim1, Monday, February 23rd
Work on problems incrementally, as we cover them in lecture (i.e. part 1)
Office Hours for help
Work alone
Work alone, BUT use your resources
  Lab Section, Piazza.com, Office Hours
  Class notes, book, Sections, CSUGLab

## Slide 4: Announcements
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2015sp/schedule.html
Slides and Reading for lectures
Office Hours
Pictures of all TAs
Homework and Programming Assignments
Dates to keep in Mind
  Prelims: Tue Mar 3rd and Thur April 30th
  Lab 1: Due this Friday, Feb 13th before Winter break
  Proj2: Due Thur Mar 26th before Spring break
  Final Project: Due when final would be (not known until Feb 14th)
Schedule is subject to change

## Slide 5: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 6: Big Picture: Building a Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 7: Goal for Today
Understanding the basics of a processor
  We now have enough building blocks to build machines that can perform non-trivial computational tasks
  Putting it all together:
  Arithmetic Logic Unit (ALU)—Lab0 & 1, Lecture 2 & 3
  Register File—Lecture 4 and 5
  Memory—Lecture 5
    SRAM: cache
    DRAM: main memory
  Instruction-types
  Instruction Datapaths

## Slide 8: MIPS Register File
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 9: MIPS Register file
MIPS register file
  32 registers, 32-bits each (with r0 wired to zero)
  Write port indexed via RW
    Writes occur on falling edge but only if WE is high
  Read ports indexed via RA, RB
Dual-Read-Port Single-Write-Port
32 x 32 Register File
QA
QB
DW
RW
RA
RB
WE
32
32
32
1
5
5
5

## Slide 10: MIPS Register file
MIPS register file
  32 registers, 32-bits each (with r0 wired to zero)
  Write port indexed via RW
    Writes occur on falling edge but only if WE is high
  Read ports indexed via RA, RB
A
B
W
RW
RA
RB
WE
32
32
32
1
5
5
5
r1
r2
…
r31

## Slide 11: MIPS Register file
Registers
  Numbered from 0 to 31.
  Each register can be referred by number or name.
  $0, $1, $2, $3 … $31
  Or, by convention, each register has a name.
    $16 - $23  $s0 - $s7
    $8 - $15  $t0 - $t7
    $0 is always $zero.
    Patterson and Hennessy p105.

## Slide 12: MIPS Memory
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 13: MIPS Memory
MIPS Memory
  32-bit address
  32-bit data (but byte addressed)
  Enable + 2 bit memory control (mc)
    00: read word (4 byte aligned)
    01: write byte
    10: write halfword (2 byte aligned)
    11: write word (4 byte aligned)
memory
32
addr
2
mc
32
32
E
Din
Dout
 | 0x00000000
 | 0x00000001
 | 0x00000002
 | 0x00000003
 | 0x00000004
 | 0x00000005
 | 0x00000006
 | 0x00000007
 | 0x00000008
 | 0x00000009
 | 0x0000000a
 | 0x0000000b
 | ...
 | 0xffffffff
0x05

## Slide 14: Putting it all together: Basic Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu
Notes: A processor executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  Harvard architecture: separate insts and data
  von Neumann architecture: combined inst and data
A bus connects the two

## Slide 15: To make a computer
Need a program
Stored program computer
Architectures
von Neumann architecture
Harvard (modified) architecture
Notes: A stored-program computer is one which stores program instructions in electronic memory. Often the definition is extended with the requirement that the treatment of programs and data in

## Slide 16: To make a computer
Need a program
Stored program computer
(a Universal Turing Machine)
Architectures
von Neumann architecture
Harvard (modified) architecture
Notes: A stored-program computer is one which stores program instructions in electronic memory. Often the definition is extended with the requirement that the treatment of programs and data in
http://en.wikipedia.org/wiki/Universal_Turing_machine#Stored-program_computer
Davis makes a persuasive argument that Turing's conception of what is now known as "the stored-program computer", of placing the "action table"—the instructions for the machine—in the same "memory" as the input data, strongly influenced John von Neumann's conception of the first American discrete-symbol (as opposed to analog) computer—the EDVAC (Electronic Discrete Variable Automatic Computer) [previous machine, ENIAC (Electronic Numerical Integrator And Computer), was not a stored-program computer, and was not even in binary, it was in decimal].
See video on von Neumann describe the stored-program computer, 34 minutes into video, https://www.youtube.com/watch?v=VTS9O0CoVng
Also, see clip on Turing in the movie The Imitation Game where Turing states that the Bombe will work in breaking the Enigma machine: https://www.youtube.com/watch?v=MM47hsaYWZE

## Slide 17: Putting it all together: Basic Processor
Let’s build a MIPS CPU
  …but using (modified) Harvard architecture
CPU
Registers
Data Memory
data, address,
control
ALU
Control
00100000001
00100000010
00010000100
...
Program Memory
10100010000
10110000011
00100010101
...
Notes: The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data. --- http://en.wikipedia.org/wiki/Harvard_architecture
Under pure von Neumann architecture the CPU can be either reading an instruction or reading/writing data from/to the memory. Both cannot occur at the same time since the instructions and data use the same bus system. In a computer using the Harvard architecture, the CPU can both read an instruction and perform a data memory access at the same time, even without a cache. A Harvard architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway .
Also, a Harvard architecture machine has distinct code and data address spaces: instruction address zero is not the same as data address zero. Instruction address zero might identify a twenty-four bit value, while data address zero might indicate an eight bit byte that isn't part of that twenty-four bit value.
A modified Harvard architecture machine is very much like a Harvard architecture machine, but it relaxes the strict separation between instruction and data while still letting the CPU concurrently access two (or more) memory buses. The most common modification includes separate instruction and data caches backed by a common address space. While the CPU executes from cache, it acts as a pure Harvard machine. When accessing backing memory, it acts like a von Neumann machine (where code can be moved around like data, a powerful technique). This modification is widespread in modern processors such as the ARM architecture and X86 processors. It is sometimes loosely called a Harvard architecture, overlooking the fact that it is actually "modified".

## Slide 18: Takeaway
A processor executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  (modified) Harvard architecture: separate insts and data
  von Neumann architecture: combined inst and data
A bus connects the two
  We now have enough building blocks to build machines that can perform non-trivial computational tasks

## Slide 19: Next Goal
How to program and execute instructions on a MIPS processor?

## Slide 20: Levels of Interpretation: Instructions
Programs written in a
High Level Language
  C, Java, Python, Ruby, …
  Loops, control flow, variables
for (i = 0; i < 10; i++) printf(“go cucs”);
main: addi r2, r0, 10
addi r1, r0, 0
loop: slt r3, r1, r2
...
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
Need translation to a lower-
level computer understandable
format
  Assembly is human readable machine language
  Processors operate on Machine Language
ALU, Control, Register File, …
Machine Implementation
op=addi r0 r2 10
op=reg r1 r2 r3 func=slt

## Slide 21: Levels of Interpretation: Instructions
High Level Language
  C, Java, Python, Ruby, …
  Loops, control flow, variables
for (i = 0; i < 10; i++) printf(“go cucs”);
main: addi r2, r0, 10
addi r1, r0, 0
loop: slt r3, r1, r2
...
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
Assembly Language
  No symbols (except labels)
  One operation per statement
Machine Langauge
  Binary-encoded assembly
  Labels become addresses
ALU, Control, Register File, …
Machine Implementation
op=addi r0 r2 10
op=reg r1 r2 r3 func=slt

## Slide 22: Instruction Usage
Instructions are stored in memory, encoded in binary
A basic processor
  fetches
  decodes
  executes
one instruction at a time
pc
adder
cur inst
decode
regs
execute
addr
data
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
op=addi r0 r2 10

## Slide 23: MIPS Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes

## Slide 24: Instruction Types
Arithmetic
  add, subtract, shift left, shift right, multiply, divide
Memory
  load value from memory to a register
  store value to memory from a register
Control flow
  unconditional jumps
  conditional jumps (branches)
  jump and link (subroutine call)
Many other instructions are possible
  vector add/sub/mul/div, string operations
  manipulate coprocessor
  I/O

## Slide 25: Instruction Set Architecture
The types of operations permissible in machine language define the ISA
  MIPS: load/store, arithmetic, control flow, …
  VAX: load/store, arithmetic, control flow, strings, …
  Cray: vector operations, …
Two classes of ISAs
  Reduced Instruction Set Computers (RISC)
  Complex Instruction Set Computers (CISC)
We’ll study the MIPS ISA in this course

## Slide 26: Instruction Set Architecture
Instruction Set Architecture (ISA)
  Different CPU architecture specifies different set of instructions. Intel x86, IBM PowerPC, Sun Sparc, MIPS, etc.
MIPS
  ≈ 200 instructions, 32 bits each, 3 formats
    mostly orthogonal
  all operands in registers
    almost all are 32 bits each, can be used interchangeably
  ≈ 1 addressing mode: Mem[reg + imm]
x86 = Complex Instruction Set Computer (ClSC)
  > 1000 instructions, 1 to 15 bytes each
  operands in special registers, general purpose registers, memory, on stack, …
    can be 1, 2, 4, 8 bytes, signed or unsigned
  10s of addressing modes
    e.g. Mem[segment + reg + reg*scale + offset]

## Slide 27: Instructions
Load/store architecture
  Data must be in registers to be operated on
  Keeps hardware simple
Emphasis on efficient implementation
Integer data types:
  byte: 8 bits
  half-words: 16 bits
  words: 32 bits
MIPS supports signed and unsigned data types

## Slide 28: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 29: MIPS Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes

## Slide 30: Takeaway
A MIPS processor and ISA (instruction set architecture) is an example a Reduced Instruction Set Computers (RISC) where simplicity is key, thus enabling us to build it!!

## Slide 31: Next Goal
How are instructions executed?
What is the general datapath to execute an instruction?

## Slide 32: Instruction Usage
Instructions are stored in memory, encoded in binary
A basic processor
  fetches
  decodes
  executes
one instruction at a time
pc
adder
cur inst
decode
regs
execute
addr
data
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
op=addi r0 r2 10

## Slide 33: Five Stages of MIPS Datapath
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor

## Slide 34: Five Stages of MIPS datapath
Basic CPU execution loop
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback
Instruction types/format
Arithmetic/Register: addu $s0, $s2, $s3
Arithmetic/Immediate: slti $s0, $s2, 4
Memory: lw $s0, 20($s3)
Control/Jump: j 0xdeadbeef

## Slide 35: Stages of datapath (1/5)
Stage 1: Instruction Fetch
  Fetch 32-bit instruction from memory. (Instruction cache or memory)
  Increment PC accordingly.
    +4, byte addressing
    +N
PC
Prog.
Mem
+4
inst

## Slide 36: Stages of datapath (1/5)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor

## Slide 37: Stages of datapath (2/5)
Stage 2: Instruction Decode
  Gather data from the instruction
  Read opcode to determine instruction type and field length
  Read in data from register file
    E.g. for addu, read two registers.
    E.g. for addi, read one registers.
    E.g. for jal, read no registers.
5
5
5
control
Reg. File

## Slide 38: Stages of datapath (2/5)
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 39: Stages of datapath (2/5)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor

## Slide 40: Stages of datapath (3/5)
Stage 3: Execution (ALU)
  Useful work is done here (+, -, *, /), shift, logic operation, comparison (slt).
  Load/Store?
    lw $t2, 32($t3)
    Compute the address of the memory.
ALU

## Slide 41: Stages of datapath (3/5)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor

## Slide 42: Stages of datapath (4/5)
Stage 4: Memory access
  Used by load and store instructions only.
  Other instructions will skip this stage.
Data
Mem
If sw
Data to store
from reg to mem
R/W
If lw
Data from
memory
Target addr
from ALU

## Slide 43: Stages of datapath (4/5)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor

## Slide 44: Stages of datapath (5/5)
Stage 5:
  For instructions that need to write value to register.
  Examples: arithmetic, logic, shift, etc, load.
  Store, branches, jump??
Reg. File
PC
WriteBack
from ALU
or Memory
New instruction address
If branch or jump

## Slide 45: Stages of datapath (5/5)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB

## Slide 46: Full Datapath
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB

## Slide 47: Takeaway
The datapath for a MIPS processor has five stages:
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback
This five stage datapath is used to execute all MIPS instructions

## Slide 48: Next Goal
Specific datapaths MIPS Instructions

## Slide 49: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 50: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 51: Arithmetic Instructions
op | rs | rt | rd | - | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | func | mnemonic | description
0x0 | 0x21 | ADDU rd, rs, rt | R[rd] = R[rs] + R[rt]
0x0 | 0x23 | SUBU rd, rs, rt | R[rd] = R[rs] – R[rt]
0x0 | 0x25 | OR rd, rs, rt | R[rd] = R[rs] ¦ R[rt]
0x0 | 0x26 | XOR rd, rs, rt | R[rd] = R[rs]  R[rt]
0x0 | 0x27 | NOR rd, rs rt | R[rd] = ~ ( R[rs] ¦ R[rt] )
00000001000001100010000000100110
R-Type
ex: r4 = r8  r6 # XOR r4, r8, r6

## Slide 52: Arithmetic and Logic
5
ALU
5
5
Reg. File
PC
Prog.
Mem
inst
+4
control
Fetch
Decode
Execute
Memory
WB
skip
r8
r6
xor
r4
xor
ex: r4 = r8  r6 # XOR r4, r8, r6

## Slide 53
Instruction fetch + decode + ALU
= Babbage’s engine
+ speed
+ reliability
– hand crank
Notes: A Babbage engine allows the values of the polynomial to be produced without ever having to multiply. A babbage engine only needs to be able to add!
This is why a babbage engine is also called a difference engine
A Babbage Engine (Difference Engine) is an automatic, mechanical calculator designed to tabulate polynomial functions. Both logarithmic and trigonometric functions can be approximated by polynomials, so a difference engine can compute many useful sets of numbers. -- http://en.wikipedia.org/wiki/Difference_engine

## Slide 54: Arithmetic Instructions: Shift
op | - | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | func | mnemonic | description
0x0 | 0x0 | SLL rd, rt, shamt | R[rd] = R[rt] << shamt
0x0 | 0x2 | SRL rd, rt, shamt | R[rd] = R[rt] >>> shamt (zero ext.)
0x0 | 0x3 | SRA rd, rt, shamt | R[rd] = R[rt] >> shamt (sign ext.)
00000000000001000100000110000000
ex: r8 = r4 * 64 # SLL r8, r4, 6
r8 = r4 << 6
R-Type

## Slide 55: Shift
5
ALU
5
5
Reg. File
PC
Prog.
Mem
inst
+4
shamt
control
r4
shamt = 6
r8
sll
sll
ex: r8 = r4 * 64 # SLL r8, r4, 6
r8 = r4 << 6
Fetch
Decode
Execute
Memory
WB
skip

## Slide 56: Arithmetic Instructions: Immediates
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + imm
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & imm
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ imm
op | rs | rd | immediate
6 bits | 5 bits | 5 bits | 16 bits
00100100101001010000000000000101
I-Type
ex: r5 += -1
ex: r5 += 65535
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + sign_extend(imm)
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & zero_extend(imm)
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ zero_extend(imm)
ex: r5 = r5 + 5 # ADDIU r5, r5, 5
r5 += 5
What if immediate is negative?

## Slide 57: Immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
inst
control
r5
r5
addiu
addiu
5
ex: r5 = r5 + 5 # ADDIU r5, r5, 5
r5 += 5
Fetch
Decode
Execute
Memory
WB
skip

## Slide 58: Immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
inst
control
r5
r5
addiu
addiu
5
ex: r5 = r5 + 5 # ADDIU r5, r5, 5
r5 += 5
Fetch
Decode
Execute
Memory
WB
skip

## Slide 59: Arithmetic Instructions: Immediates
op | mnemonic | description
0xF | LUI rd, imm | R[rd] = imm << 16
op | - | rd | immediate
6 bits | 5 bits | 5 bits | 16 bits
00111100000001010000000000000101
I-Type
ex: LUI r5, 0xdead
ORI r5, r5 0xbeef
ex: r5 = 0x50000 # LUI r5, 5
What does r5 = ?
r5 = 0xdeadbeef

## Slide 60: Immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
inst
16
control
r5
liu
liu
5
ex: r5 = 0x50000 # LUI r5, 5
Fetch
Decode
Execute
Memory
WB
skip
Notes: or, extra input to alu B mux from before/after extend
(or, extra mux after alu)

## Slide 61: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute
Next
Time

## Slide 62: Summary
We have all that it takes to build a processor!
  Arithmetic Logic Unit (ALU)—Lab0 & 1, Lecture 2 & 3
  Register File—Lecture 4 and 5
  Memory—Lecture 5
    SRAM: cache
    DRAM: main memory
A MIPS processor and ISA (instruction set architecture) is an example a Reduced Instruction Set Computers (RISC) where simplicity is key, thus enabling us to build it!!
We know the data path for the MIPS ISA
register and memory instructions